START	everyone; FM synth sound 1; quick, abrupt	gestures

CUE 1	one player; recorded sound; circular gestures

CUE 2	+player; FM synth sound 1; short bursts of	movement

CUE 3	+player; recorded sound; slow linear movement

CUE 4	increase activity and movement;
+player(s) that left; FM synth sound 2; slow linear	gestures

CUE 5	-all players with synths, one by one

CUE 6	-rest of the players

CUE 7	+player (1-3); shifter; striking gestures

CUE 8	shifter: slow linear movements.
+player (1-3); synth sound 1; quick, abrupt	gestures

CUE 9	-all players with shifter, one by one

CUE 10	synth: sound 4; very slow, almost no movement

CUE 11	+player (1-3); recorded sound; hectic and frantic	gestures

CUE 12	+rest of the players; synth sound 2; quick,	abrupt gestures

CUE 13	players with recoded sounds (cue 11): very slow,	almost no movement

CUE 14	-all players with synths, one by one

CUE 15	+player (1-3); shifter; linear gestures

CUE 16	increase activity

CUE 17	+rest of the players; synth; circular movement
all very active

CUE 18	decrease activity, gestures get slower

CUE 19	-all players with recoded sounds, one by one

CUE 20	-all players with synths, one by one.

CUE 21	one players; shifter; very slow, almost no	movement

END	all sound off

FARBENKLANGSPIEL

For any number of laptops, with one person conducting.

The MAX/MSP patch used by the laptops has a sound component and a video component.

Performers can play sounds from 3 different inputs:
FM synth, pre-recoded sound files, and pitch shifter (processing the same sound files)

FM synth has four pre-programmed sounds, but it also allows the performer have control over the synthesized sound. Click “Show FM Synth” to bring it up.

During the performance, pitches of the synthesized sound are controlled by the video color tracking.

The five pre-recoded sounds cannot be modified, but are processed by using video color tracking.
In this case, it controls playback speed, and Pitch Shifter's pitch, delay, and feedback.

To activate color tracking, click on the desired color to track in the picture on the left (showing the video input.)
The picture on the right shows a processed video input, highlighting the tracked color.
Color tracking works best with bright colors, glow sticks, LEDs, or infra red.

Generally, performers can choose what sounds to play, unless a specific one is indicated by the conductor.

For the conductor:

The conductor uses a text score with cues to the performers.

+/- adding/taking out performers. Can be signaled by traditional cue gestures. A “cut throat” gesture can be used for taking out players.

Sound input can be indicated by a number with the right hand: 1 = FM synth 2 = recorded sound 3 = shifter

Specific sound can be indicated by a number with the left hand.

The conductor can show the movement or gesture, to be imitated by the performers.

Activity, increase or decrease, can be indicated by traditional dynamic gestures.

The traditional release signal can be used to end the piece.

Ensembles are welcome to come up with any other methods.

The duration of the piece is indeterminate.